## Slide 1: CO2 fangst og lagring Principper, teknik og potentiale
Center for Energy Resources Engineering (CERE)
Department of Chemical Engineering
Technical University of Denmark (DTU)
Philip Loldrup Fosbøl
Supported by many innovative colleagues

## Slide 2: Emissions from buildings
World:
  Total GHG: 50 GT
  Total CO2: 37 GT
Buildings:
  14 GT
  Construction: 0.1 GT
CO2 Source:
  Materials + power/heat
Source: UNEP, 2020
of 37 GT
Notes: UNEP emission from building and construction 2020, right figure, only CO2 not GHG total 37GT

## Slide 3: Future: Negative CO2 emissions
Source: IPPC, https://report.ipcc.ch/sr15/pdf/sr15_spm_final.pdf, side 19
Notes: http://www.globalcarbonproject.org/carbonbudget/17/presentation.htm

## Slide 4: Current CO2 utilization
35 Gton CO2
Emissions
0.3 Gton CO2
Utilization (1%)
Source: E. Alper, O. Yuksel Orhan / Petroleum 3 (2017) 109

## Slide 5: Challenges in the future
3 Gton CO2
Current utilization (0.3 Gton)+
Synthetic fuel (1 Gton) +
All plastic (1 Gton) +
Other (0.7 Gton)
35 Gton CO2
Emissions
Source: PlasticEurope, 2015
Notes: https://committee.iso.org/files/live/sites/tc61/files/The%20Plastic%20Industry%20Berlin%20Aug%202016%20-%20Copy.pdf

## Slide 6: Future challenges – negative emissions
IPCC negative
22 Gton
Climate goal
35 Gton CO2
Emissions
We must remove CO2 from the atmosphere
Utillization is OK, but we must do it even better

## Slide 7: CO2 utilization (CCU(S))
CO2
CO2
CO2
CO2
CO2
CO2
biomass/
waste
Substitution of
fossil fuel
Energy storage
H2
CO2

## Slide 8: CCS/BECCS/DAC: CO2 capture and storage – Negative emission
CO2
CO2
CO2
BECCS
(Bio-Energy with Carbon Capture & Storage)
CO2
CO2
CO2
biomass/
waste
2.5 km
CO2
CO2
CO2
CO2
CO2
CO2

## Slide 9: Negative emissions is not obtained by CO2 conversion or using CCS on fossil fuel Negative emissions are only obtained by storing green CO2
CO2 removal from biomass power
CO2 removal from Biogas
CO2 removal from green waste combustion
Direct Air Capture (DAC)
DK emissions: 52.4 MTCO2eq
Farming: 10.3 MTCO2eq
Cement: 1.0 MTCO2eq
Notes: https://dce2.au.dk/pub/SR231.pdf
https://cdr.eionet.europa.eu/dk/Air_Emission_Inventories/Submission_UNFCCC/

## Slide 10: CO2 capture
Advantage: very high TRL
Challenge: noticeable energy use
Clean gas
Pure
CO2
Absorber
Reboil
HE
Desorber
CO2
Capture Solvent
Industrial gas
Industrial
gas

## Slide 11: Gas separation technologies being applied
Solvent based capture (single phase, VSLE, VLLE)
  Amines
  Ammonia
  Ionic liquids
  Amino acids
  Alkali (Potassium Carbonate)
  Promoters
  Enzymes (carbonic anhydradrases)
  Physical sorbent
Carbon/calcium looping
Membranes (ceramic and polymers)
Hydrates
Algae
Zeolites (adsorption)
Cryogenic freeze precipitation
Electrochemical
Rotating devices (integrated/high-speed)
Combined SOx and CO2

## Slide 12: DTU focus
Biogas upgrading
Power industry (biomass combustion)
Cement production
Steel industry
Silicium production
Paper industry
Direct Air Capture (DAC)
Refining
Fermentation
Ethanol production
Ammonia Production
Aluminium production
Natural gas cleaning
Hydrogen production
Large navy industry
Combined SO2 and CO2 removal
Acid gas treatment

## Slide 13: On-site capture testing, 1 ton/day

## Slide 14: ARC: 62 mil DKK Net Zero Carbon Capture Eneergy consumption
Objectives
  Waste heat
  Heat integration
  Cost effectiveness
Pilot
Demonstration
Full scale design
  0.48 mtpa

## Slide 16
Chalk
Sandstone
Total
Ineos

## Slide 17: Siri Area storage Potentiale Ineos prediction - Greensand
CO2-store | Statement of Feasibility | Pilot | CO2 Ready | mta
Nini West | 2020 | 2022 | 2024 | 0,45
Nini Main | 2021 | Not required | 2024 | 1
Nini Ty | 2021 | 2022 | 2024 | 0,5
Cecilie Ty | 2021 | 2023 | 2025 | 0,5
Cecilie Aqu | 2022 | 2023 | 2027 | 1
Nini East | 2022 | Not required | 2027 | 1
Stine Seg 2 | 2022 | 2023 | 2025 | 2
Siri Main | 2023 | 2023 | 2028 | 3
Total |  |  |  | 9,5
Safety |  |  |  | 4,5
Greensand
Sandstone
Nini Field
Siri area
Source: Ineos DK

## Slide 18: Larger point emitters
Fynsværket
(362MWe, 475MWt
1.2mt)
Nordjylland
(383MW, 420MWt)
Herningværket
(95MWe, 174MWt)
Skærbækværket
(392MWe, 447MWt)
Aalborg portland
(2mtCO2)
Asnærværket
(147MWe, 100MWt)
Esbjergværket
(378MWe, 420MWt)
Avedøreværket
(820MWe, 900MWt)
Amagerværket
(330MWe, 580MWt)
Kundbyværket
(710MWe)
ARC
(0.4mta)
Vestforbrændingen
(0.6mta)
KARA
(0.3mta)
Approx 800 km
Approx 280 km
Negative emission potential
Centralised : 11 mil. ton CO2
Total: 18 mil. ton CO2
DK storage potential: 22.000 Mil. Ton
1000 years
Project GREENSAND
Source: GEUS

## Slide 19: The 3D EU project
DTU objective: compression & liquefaction
19 mill EURO project

## Slide 20: A DK CCS hub – time perspective
Source: Ineos DK

## Slide 21: CCS, is it possible? Yes, Canada and Norway are doing it

## Slide 22: CCS – 1st generation exists

## Slide 23: The Danish paradoxical CO2 issues
DK guvernement focus 9 mta, possible: 4.5 mta, funding for 1 mta
Negative emission has no financial support
Offshore licenses do not allow permanent storage
Waste heat re-use is not feasible
Waste incineration plants: illegal CO2 removal
No economic incentives to produce green cement or fuel
  Regulatory use
Missing CO2 market pull/push
  No producers, no consumers, CO2 hub
Power price too high
  Hydrogen price, grid/tax issue

## Slide 24: Thank you